## Slide 1: ASKAP polarisation calibration and characterisation: The state of play
CSIRO Astronomy and Space Science, Perth astrophysics group
Craig Anderson | Bolton Fellow | CSIRO
POSSUM busy week, May 2019

## Slide 2: Whetting the collective appetite…
Fomalont+ (1995)

## Slide 3: Whetting the collective appetite…
(FORNAX A / P / ASKAP-36 / Anderson, Lenc)

## Slide 4: Whetting the collective appetite…
We now have deep (~10s -- 100 uJy/b), full-pol ASKAP-36 obs ‘in the can’ for fields:
— The LMC, SMC
— GAMA fields: G09, G12, G23
— SHAP1
— SPARCS nth
— SCORPIO (Gal. field; 0.8, 1.4 AND 1.6 GHz)
— ERIDANUS
— FORNAX
— SN1006
.
.
.
PLUS…
— The whole southern sky (Rapid ASKAP Continuum Survey; ~250 uJy/b in Stokes I; likely better in pol) .

## Slide 5: The ASKAP philosophy

## Slide 6: The ASKAP POL CAL philosophy
- No pol/sec cals for ASKAP observations (overheads for 36 beams)
- So:
Flux + bp + (on-beam-axis) leakage from B1934-638 primary cal
- But still need to cal:
XY phase (1934 is unpolarised)
Off-axis pol response
Ionospheric Faraday rotation
- XY phase is the big first order effect
- Use ‘rotated PAFs method’ to solve for (”process_polcal.py” pipeline)

## Slide 7: The ASKAP POL CAL philosophy
- No pol/sec cals for ASKAP observations (overheads for 36 beams)
- So:
Flux + bp + (on-beam-axis) leakage from B1934-638 primary cal
- But still need to cal:
XY phase (1934 is unpolarised)
Off-axis pol response
Ionospheric Faraday rotation
- XY phase is the big first order effect
- Use ‘rotated PAFs method’ to solve for (”process_polcal.py” pipeline)
OBSOLETE!

## Slide 8: Where we’re at: Current methods and results for pol processing

## Slide 9: XY-phase cal directly via beamforming
ASKAP on-dish noise radiator (ODC)

## Slide 10: XY-phase cal directly via beamforming

## Slide 11: XY-phase cal directly via beamforming

## Slide 12: Uncalibrated on-axis leakages, post beamforming

## Slide 13: Pol data quality (post-on-axis cal)
P
(Lenc, Heald, Anderson, Gaensler)

## Slide 14: Pol data quality (post-on-axis cal)
NVSS vs. ASKAP RMs

## Slide 15: Angle consistency b/w beams
Credit: Cameron van Eck
Off-axis leakage characterisation / mitigation / correction

## Slide 16: Frac. pol. vs. beam position
Credit: Xiaohui Sun
Off-axis leakage characterisation / mitigation / correction

## Slide 17: Where we’re going: Impending/future methods and measurements for ASKAP pol. obs.

## Slide 18: Leakage considerations
POSSUM Spec:
- 0.3% of Stokes I (required)
- 0.1% desirable

## Slide 19: Possibility to calibrate on-axis leakage via beamforming

## Slide 20
Max S/N beam
Shape constrained beam
ASKAP-12 holography (Hegarty + Hotan)
Possibility to calibrate off-axis leakage via beamforming

## Slide 21: Alternative: Off-axis pol corrections in image plane
(Anderson)
Uncorrected
Alternative: Off-axis pol corrections in image plane

## Slide 22
Corrected
Alternative: Off-axis pol corrections in image plane

## Slide 23: Alternative: Off-axis pol corrections in image plane
Corrected
Uncorrected

## Slide 24: (Eventual) alternative (?): AW-projection
- The ‘correct’ way
- Being investigated (Chris Skipper), but too computationally expensive to implement for routine ASKAP proc?
- Certainly will not be available for RACS or the SST pilots

## Slide 25: Practical outstanding issues

## Slide 26: Calibration: Incorporate on-axis leakage cal. in ASKAP data proc. pipeline
- We do not do this yet, but we soon need to
- ASKAPsoft can do it, so should be a relatively straight-forward re-tooling of the pipeline. But some issues like: freq dep, or freq indep? Verification/tolerances prior to pol imaging?
- I have ‘bolt on’ python scripts that can do it. Interim solution for RACS, or unnecessary (modding the normal PL is quick and easy enough)?

## Slide 27: Calibration: Abs. pol. angle
- We do not do this yet, but we soon need to
- POSSUM spec. left unspecified (1 deg. accuracy listed as ‘desirable’)
- Methods: On-dish cal system? Pseudo-one-time (e.g. at beamforming) pol. cal. visit? If so, then what (e.g. Lunar rim, point source)? More elaborate strategy?

## Slide 28: Calibration: Off-axis cross-pol response
- We do not do this yet, but we soon need to
- POSSUM spec: Good to 0.3% of Stokes I across the field
- Will need a detailed plan + concerted effort to characterize, correct, and verify.
- Methods: Image plane correction most probable for RACS and pilot (as discussed above), and characterization discussed more below.

## Slide 29: Calibration: Ion. FR
Credit: Tony Willis
Credit: Chris Riseley
- We do not do this yet, but will eventually need to
- Currently at Solar minimum, so hard to even detect, let alone correct and verify
- Methods: As discussed in detail ~2 POSSUM bw’s ago. Visibility correction with some as-yet unspecified cadence would be best-practice

## Slide 30: Data proc: Channelisation + CLEANing
- Pol. data cubes are imaged and CLEANed in 1 MHz channels, with only a limited form of masking available (two-step shallow-then-deep CLEAN; deep CLEAN at position of shallow clean comps on a per image basis)
- NOT IDEAL! (only allows for ‘proper’ decon. of bright-ish point sources; syn. beam. artifacts clearly visible post RM-synthesis for middle-bright sources, no ‘complex clean’).
- Could image in coarser channels, but trade-off with sensitivity to high RMs (esp. in low freq band; ~700 MHz low edge freq.), and is ‘kicking the can down the road’ in some sense
- More sophisticated methods exist or have been proposed (cf. wsclean -- ‘broadband squared-channel + polarisation joining’; GH’s ‘RM synthesis CLEAN’ idea) that reduce the effect of the choice of channelization, but these are not on the SDP radar right now.
- Need to decide on best (read: satisfactory + realistic) approach.

## Slide 31: Data proc: Common-resolution convolution
- Data cubes are imaged up in 1 MHz chans at their ‘native resolution’, which is freq-dependent
- Can specify a common freq indep restoring beam, but this is bad practice for several reasons
- Need to convolve the CEANed maps to a common resolution (LR would say we need to convolve the DIRTY maps to a common resolution ?!)
- We have custom scripts for this, which we’ll likely need to ‘bolt on’ to the pipeline, esp. for RACS data proc.

## Slide 32: Data proc: Polarisation DQA
Credit: Jennifer West

## Slide 33: Characterisation: Off axis leakage
- Further off-axis leakage characterisation: Pol cal “raster” scan across ¼ of the beam footprint

## Slide 34: Characterisation: Ion. FR
- Joint MWA-ASKAP tracking of ‘exclamation mark source’ for ionospheric FR detection/correction

## Slide 35: Take-aways
- How to channelise + CLEAN full-pol datacubes
- Flagging consistency across beams, sky area, Stokes params
- Pol-specific automated DQA
- AW-projection for off-axis full-Stokes imaging?
- Absolute angle calibration
- Exact implementation of IFR correction
- ASKAP is an excellent polarisation machine
- PAFs provide exceptional performance and versatility for full-pol observing
Selected issues requiring better implementation/further thought: